NUMERICAL CALCULATIONS OF GENERATION AND EVOLUTION OF THE CURRENT FILAMENTS

A.V. Gordeev, *T.V. Losseva

RRC “Kurchatov Institute”, Moscow, Russia, e-mail: gordeev@dap.kiae.ru
*Institute of Geospheres Dynamics RAS, Moscow, Russia, e-mail: losseva@idg.chph.ras.ru

Long ago, an idea of the current filaments went to the current plasma physics and allows the interpretation of many important features of the plasma dynamics in the magnetic field [1, 2]. In recent years the use of this concept in relation to the nonquasineutral current filaments gives the possibility to obtain the theoretical results connected with the generation of the high-energy particles in Z-pinches and laser plasma physics [3]. The further development of these theoretical investigations results in the nonthermal model of the hot spot, where the nonquasineutral current filaments were used [4].  Such filaments that arise on the times on the order of the inverse electron – ion collision frequency enable the interpretation of the hard x-ray emission in the experiments with X-pinch both the qualitative and quantitative one [5, 6]. It is known that the quasiequilibrium of the nonquasineutral current filament with the azimuthal magnetic field is completely determined by the Lagrangian invariant’s profile, where. One must stress that the Lagrangian invariant is defined through the electron vorticity  which is generated in the earlier stage of the plasma evolution as a result of the kinetic plasma instability by Weibel  [7] and  by the hydrodynamic approach  due to the non-collinearity of the vectors and  ( ne and pe are the plasma density and pressure) and/or due to the dissipative effects. So far the Lagrangian invariant is usually given by some reasonable profile [3]. In the presented paper we conducted the calculations of the arising of the electron vorticity by the account of the electron-ion collisions. 
This paper was supported in part within the framework of the Initiative Projects in RRC “Kurchatov institute” and NSh-1253.2008.02.

References

- Koshelev K.N., Pereira N.R. // J.Appl.Phys.1991, V.69, p.21.

- Bulanov S.V., Califano F., Dudnikova G.I., et al. // Rev. Plasma Phys.V.22 / Ed.by V.D.Shafranov. New York: Kluver Academic, 2001, p.227.

- Gordeev A.V., Losseva T.V. // Plasma Physics Reports 2005, V.31, P.26.

- Gordeev A.V., Losseva T.V. // 35-th  Intern. (Zvenigorod)  Conf. on  Plasma physics and Fusion, 2008, Absracts, p.167.

- Gordeev A.V., Losseva T.V. // 17-th Int. Conf. on High-Power Particles Beams. Xi’an, China, 2008. Paper 07-O-04.  Conf. Guide and Absracts, p.6.

- Gordeev A.V., Losseva T.V. // Plasma Physics Reports, 2009 , V.35, N 2 (in press).

- Weibel E.W. // Phys. Rev. Lett.1959, V.2, p.83.