Технические особенности проекта импульсного генератора на основе индуктивного накопителя и комбинированного размыкателя тока

Егоров О.Г.

ГНЦ РФ ТРИНИТИ, г.Троицк, , Московская обл., Россия, egorov@triniti.ru

В работах [1-4] представлены к рассмотрению составные части проекта разрабатываемого наносекундного генератора импульсов на основе индуктивного накопителя. Генерация импульсов основана на усовершенствованной комбинации вакуумного размыкателя и плазменного прерывателя тока (КРТ), а также свойствах индуктивного накопителя. В состав конструкции КРТ входит -стабилизатор тока, -схема перевода тока из контактной части в разрядную часть, -схема паузы тока с преобразованием в генератор Маркса. Вторая важная часть проекта - схема умножения тока. Для этого в проекте предлагается использовать трансформаторный накопитель. Учитывая особенности конструкции размыкателя и накопителя умножение тока возможно посредством экранирования первичной обмотки в момент вывода энергии.

В статье рассмотрены возможные варианты технической реализации проекта, а именно конструктивные особенности индуктивного накопителя. В частности, предложены вниманию конструктивные варианты вывода энергии из индуктивного накопителя. Дан анализ преимуществ и недостатков этих вариантов.

Литература

Egorov O.G. Distribution of magnetic field in combined opening switch (vacuum interrupter and plasma opening switch) on energy storage stage in inductance.//Proc. the X International on Megagauss Magnetic Field Generation and Related Topic, Berlin, Germany, July, 2004.

Egorov O.G.  The conception of high power pulsed compact generator based on inductive storage and combined opening switch //Proc. International Conference “Zababakhin science talking”, Sneginsk, Russia, September, 2007.

Egorov O.G. Development of the conception of high power pulsed compact generator based on inductive storage and combined opening switch // 2th Proc. Euro-Asian International Pulsed Power Conference, Vilnius,  Lithuania, September, 2008.

Egorov O.G. The Project of pulse power generator based an inductive storage and a combination of vacuum interrupter and plasma opening switch// Proc. the IET European Pulsed power Conference, CERN, Geneva, Switzerland, September, 2009.