MICROWAVE ULTRAVIOLET LAMP

E.M. Barkhudarov, M.A. Misakyan, I.A. Kossyi, V.A. Kiselev*, I.M. Taktakishvili, A.V. Tulupov*

General Physics Institute of Russian Academy of Sciences, Moscow, Russia
*“SOLITON-NTT” Co. Ltd., Moscow, Russia

Microwave gas-discharge ultraviolet lamp (MW-UV-lamp) has been built up in the Plasma Physics Division of General Physics Institute of Russian Academy of Sciences (GPI).

Unusual method of microwave discharge excitation in a lamp bulb has been developed. This method based on a principle of “truncated electrode of coaxial” has been formulated previously (see [1]) allows excite microwave discharge in gases and gaseous mixtures over a wide range of pressures at a relatively low microwave power. Ordinary magnetrons used in modern domestic microwave ovens (wavelength near 12 cm, power about 600-1000W) have been utilized in a MW-UV-lamp that is now in operation. Principles of microwave energy input in an “open” lamp as well as a lamp introduced in water have been elaborated.

The main preferences of this construction are as following:

- Absence of electrodes that noticeably increases of UV-lamp life time;

- Simplicity and cheapness of water disinfection system based on the MW-UV-lamp application.

Preliminary microbiological researches have shown that the productivity of lamp regarding to the disinfection of microbially contaminated water (reduction of microbial content in ( 103 less than the initial one) is as low as:

( ( 10-3 kW hour/liter.

For experimental investigation of spectral characteristics of MW-UV-lamp optical and chemical (actinometric) methods developed in GPI (see [2,3]) have been targeted for application. With help of these methods optimal buffer gas pressure for biologically active UV radiation has been determined.

References

S.I. Gritsinin, I.A. Kossyi et al,  Proceedings of 14th International Symposium on Plasma Chemistry, Prague, 1999, v. II, 675.

Yu.B. Bark, E.M. Barkhudarov, I.A. Kossyi et al., J. Phys. D: Appl. Phys., v. 33, 2000, 859.

A.M. Anpilov, E.M. Barkhudarov, Yu.B. Bark et al,  J. Phys. D: Appl. Phys., v. 34, 2001,  993.