Fireball Ejection from a Molten Hot-Spot in Solid to Air by a Reversed Microwave Drill Mechanism

Eli Jerby( and Vladimir Dikhtyar

Faculty of Engineering, Tel Aviv University, Ramat Aviv 69978, Israel

The paper presents experimental observations of fireball ejection from hot spots in solid materials to the atmosphere [1]. The hot spot is created in the solid substrate material (silicon, germanium, glass, ceramics, basalt, etc.) by near-field concentrated microwaves [2]. The vaporized drop evolving from the hot spot is blown up, and forms a stable fireball buoyant in the air [3]. The fireballs observed in our experiments tend to absorb the available microwave power entirely, in an adaptive manner. They exhibit some features of natural ball-lighting phenomena, and could be related also to plasma confinement, lighting, combustion, and material processing techniques.

References

V. Dikhtyar and E. Jerby, "Fireball ejection from a molten hot spot to air by localized microwaves," Physical Review Letters 96, 045002 (2006).

E. Jerby, V. Dikhtyar, O. Actushev, U. Grosglick, "The microwave drill,"  Science 298, 587 (2002).

See video clips at http://www.eng.tau.ac.il/~jerby/Fireballs.html

# Footnotes

- Corresponding author – e-mail: jerby@eng.tau.ac.il